## Slide 1: Microprocessors and Interfacing
Presenters
Asiimwe Elvis - BU/UP/2021/O343
Obbo Livingstone - BU/UP/2021/1300

## Slide 2: Topic: Microprocessor Functions
Data processing (Arithmetic and logical operations)
Control and managent of peripheral devices
Communication between different system components
Memory management
Instruction execution - fetch, decode, execute instructions from software programs
Input/Output operations from various devices

## Slide 3: cont..
Data handling: handles data transfer between registers, memory and I/O devices.
Control signals: generates control signals to cordinate operations.
Pipelining: pipelines processes to enable simultaneous processing
Instruction types: handles different instruction types based on the microprocessor architecture.

## Slide 4: cont..
the above mention tasks are manage by different functional units namely;
Exection Unit
Bus Interface Unit

## Slide 5: Execution Unit
This refers to a critical component responsible for the execution of instructions.
This has no direct connection to the system buses and uses the instruction decoder and Arithmetic Logic Unit (ALU) to control operations on data by ;
It takes in the decoded instructions from the instruction decode stage and gives instructions to the BIU stating from where the instruction are fetched.
Execution is then done based on the instructions.

## Slide 6: Functional Parts of the Execution Unit
Arithmetic Logic Unit
Handles all arithmetic and logical operations such as addition, subtraction multiplication division etc.
Stack Pointer Register
Is a 16-bit register which holds the address from the start of the segment to the memory location where a word was most recently stored on the stack. The stack is a region for storing temporary data e.g function parameters, return addresses, and local variables. It points to the current top of the stack thus enabling the microprocessor to keep track of where data is being pushed onto or popped off the stack.
Flag Regster
Is a 16 bit rigester which changes its status according to the resuLts stored in the accumulator
It has 9 flags divided into two i.e
Coonditional Flags
This represents the results of the last arithmetic or logical instruction executed and is subdivided into;
carry flag: Inicates an overflow condition for arithmetic operations
auxilliary flag: Used by carry processor to perform binary BCD conversions
parity flag: Indicates the parity of a result. if even number of 1’s in the lower order 8 bits, the parity flag is set and if odd number of 1’s, its reset.
zero flag: this is set to 1 when the results of the arithmetic or logical operation is zero else it is set to 0.
sign flag: holds the sign of the result such that if result is negative, the sign flag is set to 1 else it is set to 0
overflow flag: this represents the result when the system capacity is exceeded.

## Slide 7: cont..
Control Flag
These control the operation of the execution unit and are divided into;
trap flag: it sets single step mode used to allow execution of one instruction at a time for debugging.
interupt flag: it enables or disables interuption of programs. if set to 1 - interupt enable condition. 0 - interupt disabeled
direction flag: used in string operations and when set to 1, stirng bytes are accessed form highest to lowest memory address and vice versa.

## Slide 8: cont..
General Purpose Register
This can be used individually to store 8 bits of data and in pairs to store 16 bit data
They are of 8 types namely; AH, AL, BH, BL, CH, CL, DH and DL registers which can also be grouped into valid pairs as below;
AX (Accumulator register) - used to store operands for arithmetic operations. Pair of AL and AH form the AX used for 16-bit operations.
BX (Base register) - used to store imediate results, control information/base address of memory area within the data segement
CX (Counter register) - used in loop instructions to store loop counters.
DX - used to hold input/output port address for input/Output instructions.

## Slide 9: Bus Interface Unit
This connects the execution Unit to the system buses through the internal buses
It also manages all data and addresses transfers on the buses such as;
sending address
fetching instructions from memory
reading and writing data from/to the ports and memory
pipeline staging: fetches instructions ahead of time alowing efficient execution by the execution unit.

## Slide 10: Functional Parts
Instruction Queue
This stores up to 6 bytes of the next instructions which are read by the Execution Unit when ready for next execution.
Segment Register
These hold the addresses of instructions and data in memory used by the processor to access memory locations
It also contains one pointer register which holds the address of the next instruction to be executed by the Execution Unit;
The BIU has four segment buses namely;
Code segment - addresses the memory location in the code segment of memory where executable program is stored
Data segment - consist of data used by the program accessed by an offset address or the content of the other register that holds the offset address
Stack segment - handles memory to store data and addresses during execution
Extra segment - is an additional data segmentwhich is used by the string to hold extra destination data.

## Slide 11: cont..
Instruction Pointer
Is a 16-bit register used to hold the address of the next instruction to be executed
End!!!